| ITEM NUMBER: | name: | supplier: | DESCRIPTION: | UPDATED: |
| --- | --- | --- | --- | --- |
| 476-14 | party light 20 led | Best Season | 20led multi LED party light chain | 2012-02-22 |
| PRODUCT PHOTO/DRAWING: |
| MATERIAL SPECIFICATION: | dESCRIPTION: |
| PVC | Multi colored party light balls Black sockets with hooks Green cable |
| BULB SPECIFICATION: |
| NUMBER | INCL. | SOCKET | DESCRIPTION | RATINGS | COLOR |
| 20 pcs | yes | fixed | 5 mm LED | 3,2V 0,032W | multi |
| ITEM NUMBER | LIFE INDEX | CONNECTED | BRIDGED |
| -- | 10 000 h | 2grp, 10 pcs/grp | NO (NOT NEEDED) |
| ELECTRICAL SPECIFICATION: |
| RATING | LEAD WIRE SPEC. | LENGTH | INNERCABLE SPEC. | LENGTH |
| 24V 0,3W IP44 | 2x0,2 mm² | 500 cm | 1x0,2 mm² | 570 cm |
| WIRE COLOR | SWITCH | SWITCH COLOR | PLUG TYPE | PLUG COLOR | SPACING Pr. – Sw. – Pl. |
| green | -- | -- | 10 mm | green | -- |
| CANDLE BODY SPEC. | LAMP HOLDER SPEC. |
| -- | -- |
| LOW VOLTAGE (TRANSFORMER): |
| TYPE NUMBER | RATINGS INPUT/OUTPUT | APPROVALS | COLOR |
| MAO-2400100 | 230V/24V AC 2,4VA IP44 | s | black |
| DRAWING |
| ACCESSORIES: |
| DECORATION | SPARE BULBS | OTHERS | ASSEMBLING INSTRUCTION |
| -- | -- | -- | -- |

| MARKING PRODUCT: |
| --- |
| RATING LABEL(near the plug) |
| Marking on product: | Marking on transformer: |
| GIFTBOX: |
| BRAND | TYPE | COLOR | BOX ID. | CARDBOARD |
| star | cardboard | white | w-476-13-a | SINGLE LAYER 2 mm |
| MEAS (WxDxH ) | VOLUME | GROSS WEIGHT | PRODUCT WEIGHT | BAR CODE |
| 470 x 55 x 280 mm | 7,24 dm³ | 0,95 Kg | 0,63Kg | 7391482476142 |
| MARKING | SPECIAL MARKING (Customer related etc) |
| Item number and barcode. | - |
| EXPORT BOX: |
| UNIT/BOX | MEAS.(WxDxH) | VOLUME | WEIGHT | CARDBOARD | BARCODE |
| 6 pcs | 360 x 295 x 500 mm | 53,1 dm³ | 6,2 Kg | DOUBLE LAYER 6 mm | 17391482476149 |
| MARKING | SPECIAL MARKING (Customer related etc) |
| Star Trading shipping mark: |  |
| SHIPPING INFORMATION: |
| PORT | COUNTRY OF ORIGIN | CUSTOM CODE |
| ningbo | china | 94 05 30 0000 |
| SPECIAL PACKING INSTRUCTIONS: |
| PALLET (120;240cm): |
| UNITS/ PALLET | HEIGHT/ PALLET | WEIGHT/ PALLET |
| 0;216 pcs (EUR-PALLET) | 0;2310 mm (EUR-PALLET) | 0;249 Kg (EUR-PALLET) |
| --pcs (PAPER-PALLET) | --mm(PAPER-PALLET) | --Kg(PAPER-PALLET) |
| CONTAINER: |
| UNITS/ 20’ (28m3) | UNITS/ 40’ (58m3) | UNITS/ 40’HQ (65m3) |
| 3 160 pcs (BULK) | 6 550 pcs (BULK) | 7 350 pcs (BULK) |
| --pcs(PAPER-PALLET) | --pcs(PAPER-PALLET) | --pcs(PAPER-PALLET) |

# Text boxes

outDOOR

STAR TRADING AB

Model no.                            476-14

Transformer output:          24V 2.4VA IP 44

Bulb spec.:                         3.2V 0.032W LED

Number of bulbs:               20

Total power:                       0.25W

Production week:              1143

IP44

Star T item no ……........

Star T order no…………

Quantity in carton………

Carton number………….

Production year/week…